## Slide 1: EE724 Nanoelectronics Course Projects Collaborator: Synopsys
Optimum Device Design for NIPIN Selector
Anubhav Bhatla, Hemant Hajare and Nikhileshsing Rajput
Mentored by Hemant Kumar and Shubham Patil

## Slide 2: Outline
EE724 Nanoelectronics Course Projects, 2024
Understand Impact Ionization
Analyse
  PIN device
  NIPIN device
    Uniform charge distribution
    Delta charge distribution
Experiment NIPIN device for
  Effect of varying lengths of i1 and i2 regions
  Effect of temperature on IV characteristics
  Effect of proportion of Germanium in p-region
5 May 2024

## Slide 3: Motivation
EE724 Nanoelectronics Course Projects, 2024
Advantages of NIPIN selector over NPN selector
  NIPIN : linear band diagram, NPN : non-linear band diagram
  NIPIN : ideal subthreshold slope and negligible degradation, NPN : subthreshold slope degradation at high V
Experimental demonstration of impact ionization
High current, sub ±2V operation, voltage asymmetry
5 May 2024

## Slide 4: Device Details
EE724 Nanoelectronics Course Projects, 2024
Device consists of 5 regions : n+, i1, p+, i2, n+
i1 are i2 are p-regions but relatively intrinsic w.r.t n+ and p+
Device is symmetric/asymmetric based on if i1 and i2 have equal lengths and doping concentration
Length of p region is very small (~1 nm) as compared to other regions (~10nm)
p-region is delta-doped
Highly p- doped intrinsic region and δ-doped p+ region
5 May 2024
N+
N+
i/p-
i/p-
δp+
1020 cm-1
1019 cm-1
1016 cm-1
1016 cm-1
1020 cm-1

## Slide 5: TCAD calibration
EE724 Nanoelectronics Course Projects, 2024
5 May 2024
(sdegeo:create-rectangle
(position xminp yminp 0) (position xmaxp ymaxp 0)
"SiliconGermanium" "p"
)
HeteroInterface
MoleFraction( RegionName = ["p"]
xFraction = 1.00)
eAvalanche
hAvalanche
Impact Ionization:
Si-Ge in p-region:

## Slide 6: Impact Ionization
EE724 Nanoelectronics Course Projects, 2024
5 May 2024

## Slide 7: Impact of parameter variation
EE724 Nanoelectronics Course Projects, 2024
Length of i1 and i2 regions
  Device is symmetric/asymmetric if length of i1, i2 are equal/unequal respectively
  IV characteristics/Band diagram are symmetric/asymmetric likewise
Symmetric and asymmetric IV characteristics
5 May 2024

## Slide 8
EE724 Nanoelectronics Course Projects, 2024
5 May 2024

## Slide 9: Impact of parameter variation
EE724 Nanoelectronics Course Projects, 2024
Temperature of operation
Existence of cross over point
5 May 2024

## Slide 10: Impact of parameter variation
EE724 Nanoelectronics Course Projects, 2024
Bias voltages
Barrier height increases with positive bias
5 May 2024

## Slide 11: Impact of parameter variation
EE724 Nanoelectronics Course Projects, 2024
The hole well can be modified without modifying the electron barrier
5 May 2024
Proportion of Germanium in p-region

## Slide 12: Conclusion and future work
EE724 Nanoelectronics Course Projects, 2024
NIPIN device
  Symmetric and asymmetric properties
  Number of controllable parameters
    Width of regions
    Doping concentration
  Impact ionization
Effect of using Si-Ge in i-regions
5 May 2024

## Slide 13: Reference
EE724 Nanoelectronics Course Projects, 2024
B. Das, S. Sushama, J. Schulze and U. Ganguly, "Sub-0.2 V Impact Ionization in Si n-i-p-i-n Diode," in IEEE Transactions on Electron Devices
R. Meshram et al., "High performance triangular barrier engineered NIPIN selector for bipolar RRAM," 2014 IEEE 6th International Memory Workshop (IMW)
5 May 2024

## Slide 14: Appendix – Physics of Impact Ionization
EE724 Nanoelectronics Course Projects, 2024
5 May 2024

## Slide 15
EE724 Nanoelectronics Course Projects, 2024
5 May 2024
E<Eg

## Slide 16
EE724 Nanoelectronics Course Projects, 2024
5 May 2024

## Slide 17
EE724 Nanoelectronics Course Projects, 2024
5 May 2024
E>Eg

## Slide 18
EE724 Nanoelectronics Course Projects, 2024
5 May 2024

## Slide 19
EE724 Nanoelectronics Course Projects, 2024
5 May 2024

## Slide 20
EE724 Nanoelectronics Course Projects, 2024
5 May 2024

## Slide 21
EE724 Nanoelectronics Course Projects, 2024
5 May 2024

## Slide 22
EE724 Nanoelectronics Course Projects, 2024
5 May 2024

## Slide 23
EE724 Nanoelectronics Course Projects, 2024
5 May 2024