## Slide 1
Modelling and Analysis of PASS-P
Presented by Anubhav, 200070008
Supervisor: Prof. Virendra Singh
1
EE691: R&D Project
Computer Architecture and Dependable Systems Lab
Department of Electrical Engineering, IIT Bombay

## Slide 2
2
CORE 1
L3 Cache
LLC is shared between the two cores => Vulnerable to side-channel attacks
L1 Cache
L2 Cache
CORE 2
L1 Cache
L2 Cache
Multicore System
BUS

## Slide 3
Flush + Reload
Monitored cache lines are flushed from the cache hierarchy
Attacker waits for the victim to access cache lines
Attacker reloads flushed lines
Hit / Miss can be inferred by the access time
  If access hits => victim brought the block into the cache
  If access misses => victim did not access the line
3
“Flush+reload: A high resolution, low noise, l3 cache side-channel attack,” in Proceedings of the 23rd USENIX Conference on Security Symposium, SEC’14

## Slide 4
Prime + Probe
4
“Last-level cache side-channel attacks are practical,” in 2015 IEEE Symposium on Security and Privacy
Attacker fills (primes) cache sets with its own data
Attacker wait for the victim to access cache lines
Attacker reloads primed lines
Hit / Miss can be inferred by the access time
  If access hits => victim did not access the line
  If access misses => victim evicted the line => cache line was accessed

## Slide 5
Cache Security
Cache Randomization
  address mapping from main memory to the cache subsystem is randomized => attacker process cannot detect accesses made by the victim process
Cache Partitioning
  Static Partitioning: guarantees security, heavy performance penalty, cache lines remain under-utilized
  Dynamic Partitioning: performs better than static partitioning, susceptible to side-channel attacks
5
“Partitioned cache architecture as a side-channel defence mechanism.” Cryptology ePrint Archive, Paper 2005/280

## Slide 6
Utility-based Cache Partitioning
UCP allots more lines to the process that has a higher ‘utility’
  Utility: increase in cache hit-rate if the process was given an additional cache line
Performs better than Static partitioning in all benchmarks
6
“Utility-based cache partitioning: A low-overhead, high-performance, runtime mechanism to partition shared caches,” in MICRO 39: Proceedings of the 39th Annual IEEE/ACM International Symposium on Microarchitecture

## Slide 7
Side-Channel Threat
Reallocated lines can still be accessed by the first process until the second process overwrites them
Any side-channel attack on DCP is possible due to this reallocation
Attacker program can artificially increase or decrease its ‘utility’ to cause reallocation of cache lines to and from itself respectively
7

## Slide 8
Flush + Reload on UCP
8
V0 |  |  |  |  |  |  | 
V0 |  |  |  |  |  |  | 
V0 | V1 | V2 | V3 | V4 | V5 | V6 | 
V0 | V1 | V2 | V3 | V4 | V5 | V6 | 
FLUSH
EXECUTE
RELOAD

## Slide 9
Prime + Probe on UCP
9
V0 | A1 | A2 | A3 | A4 | A5 | A6 | A7
V0 | A1 | A2 | A3 | A4 | A5 | A6 | A7
V0 | A1 | V2 | A3 | V4 | V5 | A6 | A7
V0 | A1 | V2 | A3 | V4 | V5 | A6 | A7
PRIME
EXECUTE
PROBE

## Slide 10
Performance And Security Sensitive DCP
Security with Invalidation
Invalidates all cache lines reallocated from one core to another
Side channel attacks cannot be mounted in such a system:
  Flush + Reload: All the lines reallocated to the attacker after the Execute step will be invalidated and the attacker gets a miss for every targeted address in Reload
  Prime + Probe: The lines primed by the attacker in the Prime step are invalidated upon reallocation and the attacker gets a miss in the Probe step
Differential timing analysis fails!
10
“PASS-P: Performance and security sensitive dynamic cache partitioning,” in Proceedings of the 19th International Conference on Security and Cryptography - Volume 1: SECRYPT

## Slide 11
Flush + Reload on PASS-P
11
V0 |  |  |  |  |  |  | 
V0 |  |  |  |  |  |  | 
V0 | V1 | V2 | V3 | V4 | V5 | V6 | 
FLUSH
EXECUTE
RELOAD
V0 |  |  |  |  |  |  | 

## Slide 12
Prime + Probe on PASS-P
12
V0 | A1 | A2 | A3 | A4 | A5 | A6 | A7
V0 |  |  |  |  |  |  | A7
V0 |  | V2 |  | V4 | V5 |  | A7
PRIME
EXECUTE
PROBE
V0 |  |  |  |  |  |  | A7

## Slide 13
PASS-P
Modified-LRU Reallocation Policy
UCP: first process can still access reallocated lines until the second process overwrites them
PASS-P: due to invalidation, first process gets additional misses
Dirty reallocated lines must be written to the main memory before invalidation => surge in memory traffic at the start of each UCP phase
PASS-P preferentially re-allocates clean lines over dirty lines
13

## Slide 14
Modified-LRU Reallocation Policy
Threshold fraction (f) ∈ [0,1]
Reallocate LRU-Clean line if one exists and is in the ‘f’ fraction of the least recently used lines allocated to the process, else reallocate the LRU-Dirty line
Threshold (thr) => number of cache accesses after which the UCP is called => decides number of ways for each core
14

## Slide 15
15
 | * |  | * | * |  |  | 
 | * |  | * | * |  |  | 
UCP
PASS-P
MRU
MRU
LRU
LRU
LRU
Clean
* represents dirty block
f is assumed to be 0.75

## Slide 16
Benchmarks
16
“Memory hierarchy characterization of SPEC CPU2006 and SPEC CPU2017 on the intel xeon Skylake-SP,” PLoS One
MC Pairs | gcc_gromacs, sphinx_gromacs, astar_h264ref, omnetpp_gromacs, bzip_gobmk, wrf_h264ref, libq_sjeng
MM pairs | leslie_sphinx, astar_libq, gcc_lbm, milc_bzip, libq_milc, zeusmp_omnetpp, mcf_zeusmp, bzip_lbm, gcc_milc, omnetpp_libq, gcc_libq, gcc_soplex, leslie_astar, wrf_bwaves
Benchmarks running on two separate cores:
Both benchmarks are memory-intensive (MM pairs)
First benchmark is memory-intensive while the second is compute-intensive (MC pairs)
Distinction is made based on the APKI

## Slide 17
Simulation Setup
17
Simulator | Sniper Multicore Simulator
L1-D / L1-I Cache | 32 KB, 4-Way, LRU, Private, 4 cycles
L2 Cache | 256 KB, 8-Way, LRU, Private, 8 cycles
Last Level Cache (L3) | 4MB, 16-way, Shared, 30 cycles
Main Memory Latency | 175 cycles
Baseline Processor | x86 Nehalem microarchitecture, 2.67 GHz, 4-wide fetch,128-entry ROB

## Slide 18
Choosing the threshold fraction (f)
<number>
f = 0.75 will be considered for further evaluation
*thr is assumed to be 10k

## Slide 19
Choosing the threshold (thr)
<number>
thr = 10k will be considered for further evaluation

## Slide 20
<number>
Evaluation
Performance gain of up to 43% and 5% on average for MM pairs
Choice of partitioning doesn’t affect compute-intensive programs
Overall gain of 3.12%
1.43

## Slide 21
<number>
Sensitivity to LLC Associativity
Average performance gain increases to 4.09% for 4 ways
Lower associativity benefits more from PASS-P
=> more efficient utilization of the cache sets
* Associativity is changed while keeping cache size same

## Slide 22
<number>
Sensitivity to LLC Size
Performance gain decreases with increasing cache size
Higher cache size => working set fits better => less conflicts
=> less dependence on reallocation policy
* Cache size is changed while keeping associativity same

## Slide 23
<number>
Analysis of Clean Blocks
Percentage of Clean reallocated blocks increases from 53.8% to 59.1%
for M-M pairs as we move from UCP to PASS-P

## Slide 24
<number>
Analysis of Clean Blocks
Percentage of Clean reallocated blocks increases from 42.2% to 42.3% for M-C pairs as we move from UCP to PASS-P => M-C pairs are insensitive
to the reallocation policy used

## Slide 25
<number>
Analysis of Dead Blocks
14 out of the 21 benchmark pairs have a Dead block percentage of
more than 25% => dead blocks can be used for reallocation
=> dead block aware policies such as DAAIP
DAAIP: deadblock aware adaptive insertion policy for high performance caching,” in 2017 IEEE International Conference on Computer Design, ICCD 2017

## Slide 26
Conclusion and Future Work
PASS-P proposes invalidation of reallocated blocks to ensure security => performance loss
Preference to clean blocks helps increase the clean reallocated block percentage => performance increases
Using deadblocks for reallocation
  Deadblock Aware Adaptive Insertion Policy (DAAIP)
Preference to dead blocks for reallocation and analyze the performance with respect to PASS-P
<number>

## Slide 27
THANK YOU!
<number>